## Slide 1
HARBOR LOOP HEAT-PUMP EXPLAINER
How shared heat will
work at Harbor Loop
A plain-language guide for residents of the fictional 240-home Harbor Loop neighborhood before
installation begins.
Notes: This briefing is for interested residents who do not need a technical background. The goal is to explain the mental model, what will change at home, and what safeguards are planned before work starts.

## Slide 2
02 ANSWER FIRST
THE QUESTION
What is being installed, and what should residents expect?
ONE-SENTENCE ANSWER
The Harbor Loop network moves useful heat from the ground, upgrades it with shared electric heat pumps, and delivers normal heating
and hot water while homes keep their radiators and thermostats.
Source: user brief. Harbor Loop, the utility and all numbers are fictional.
02 / 12
Notes: The simplest picture is not a furnace in each home. It is a neighborhood heat-moving system, with electric heat pumps doing the temperature lift in each building.

## Slide 3
03 MENTAL MODEL
The system moves heat, then upgrades it
MOVE
Ground as a steady heat
source
Twelve sealed boreholes exchange
heat with the ground through water
loops 190 metres deep.
SHARE
A mild neighborhood loop
Water circulates around Harbor Loop
at 9°C to 18°C, carrying low-
temperature heat between buildings.
UPGRADE
Heat pumps raise the
temperature
Each building’s central heat pump
raises heating water to 52°C for space
heating.
SO WHAT
The network does not create heat by burning fuel in each home. It collects existing heat and lifts it to a useful temperature.
03 / 12
Notes: The ground is not a magic battery, and the heat pump is not a boiler. The useful mental model is a lift: the loop brings low-grade heat to the building, and the heat pump lifts that heat to radiator temperature.

## Slide 4
04 FIVE STAGES
Five parts work as one separated system
Same vocabulary we will use throughout: boreholes, shared ambient loop, building heat pump, domestic
hot-water booster, smart controls.
1
Twelve boreholes
190 m deep, sealed water
loops exchange heat with
the ground.
2
Shared ambient
loop
Water circulates around
the neighborhood at 9°C
to 18°C.
3
Building heat
pump
One central unit in each
of six buildings raises
heating water to 52°C.
4
Hot-water
booster
Domestic hot water
reaches 60°C, with a
weekly 65°C hygiene
cycle.
5
Smart controls
Flexible heating shifts
away from the 17:00 to
20:00 grid peak.
SEPARATION SAFEGUARD
No borehole fluid enters household water. The ground loop, heating loop and domestic-water loop are hydraulically separate.
04 / 12
Notes: This is the relationship diagram for the whole deck. The important point is that the system is connected for heat transfer, but the water circuits are kept separate.

## Slide 5
Normal radiators stay in use.
Thermostats work as before.
Residents keep their chosen set point.
Heating and hot-water service remains the goal.
Home connection takes one working day.
Planned heating interruption is four hours.
Radiators may feel warm rather than hot.
The system may run longer at lower temperature.
05 AT HOME
What changes and what stays familiar
What stays the same
What changes
WHAT WE DO NOT KNOW YET
Your exact one-day connection slot is chosen later, after survey access is confirmed.
05 / 12
Notes: The experience should still feel like normal central heating, but the radiator feel can be different. Warm for longer can be normal, because the system is designed around lower water temperatures.

## Slide 6
MONTH | USEFUL HEAT | ELECTRICITY | AVERAGE LOOP TEMPERATURE | PLAIN-LANGUAGE READING
January | 78 MWh | 25 MWh | 9°C | Highest heating need, coldest loop.
April | 42 MWh | 12 MWh | 12°C | Spring demand drops.
July | 18 MWh | 5 MWh | 17°C | Mainly hot-water demand.
October | 46 MWh | 13 MWh | 13°C | Heating season starts again.
06 SEASONAL PATTERN
Demand falls in summer, loop temperature rises
REPRESENTATIVE BUILDING, MODELED MONTHLY PATTERN
Source: user brief, representative building model.
06 / 12
Notes: This is the dense reference slide for the seasonal pattern. Residents do not need to manage these temperatures, but it helps to see why winter and summer feel different for the system.

## Slide 7
07 OPERATING CYCLE
The same loop adapts through the year
Winter
More heat is drawn from
the loop. January average
loop temperature: 9°C.
Shoulder seasons
Demand eases. April and
October sit around 12°C to
13°C.
Summer
Less space heating. July
loop average rises to 17°C.
Building heat pumps
lift temperature as needed
demand drops
season turns
heating returns
controls avoid 17:00 to 20:00 peak where flexible
07 / 12
Notes: Think of the year as a cycle, not a switch. The heat pump keeps lifting temperature to what the building needs, while the loop itself changes with the season.

## Slide 8
Chart: 
| Useful heat | Heat-pump electricity | Pumps and controls
MWh per year | 2880 | 820 | 74
08 ENERGY BALANCE
Most delivered heat is moved, not bought as electricity
2,880
MWh annual useful
heat demand
820
MWh heat-pump
electricity
74
MWh pumping and
controls
PERFORMANCE MODEL
Seasonal performance factor: 3.5 units of heat delivered per unit of heat-
pump electricity.
ANNUAL MODELED ENERGY, MWH
Source: user brief. Values are modeled for the fictional project.
08 / 12
Notes: The useful heat delivered is much larger than the heat-pump electricity input. That is the point of upgrading existing heat rather than producing all heat directly from electricity in each home.

## Slide 9
Chart: 
| Existing gas | Shared heat pump
tonnes CO2e per year | 692 | 178
Chart: 
| Gas baseline | Year-one charge
euros per month | 108 | 96
09 TRADE-OFFS
The model lowers emissions and the year-one charge
OPERATIONAL EMISSIONS
REPRESENTATIVE 78 M² HOME
TRADE-OFF TO KNOW
The service charge is indexed annually, capped at consumer inflation plus 1 percentage point for the first five years.
Source: user brief. Emissions use the fictional project’s stated electricity factor.
09 / 12
Notes: The modeled emissions fall from 692 to 178 tonnes CO2e a year. The representative year-one charge is also lower than the weather-normalized gas baseline, but it is indexed each year within the stated cap.

## Slide 10
10 A HOUSEHOLD DAY
A normal day should still feel normal
MORNING
Thermostat as usual
You set the thermostat. The building
heat pump supplies lower-
temperature heating water for longer,
steadier runs.
LATE AFTERNOON
Small pre-heat if useful
Controls may pre-heat by up to 0.7°C
before the evening peak, never above
your chosen set point.
EVENING AND NIGHT
Hot water and quiet plant
Hot water is boosted to 60°C.
Modeled nighttime level at the nearest
bedroom facade is 24 dBA.
48 dBA
normal plant-room sound at one metre
60°C
domestic hot-water booster
temperature
65°C
weekly hygiene cycle temperature
10 / 12
Notes: The thermostat remains the resident’s control point. Smart controls can shift flexible heating away from the evening peak, but the brief is clear that they do not push above the resident’s chosen set point.

## Slide 11
11 SAFEGUARDS
Safeguards cover water, heat and accountability
WATER SAFETY
Separated loops
No fluid from boreholes enters
household water. Water hygiene is
verified before handover.
RESILIENCE
Backup heat
Backup electric boilers cover the
coldest 18 modeled hours a year and
provide N+1 resilience during
maintenance.
SUPPORT
Loss-of-heat response
A 24-hour support line responds
within 30 minutes and targets
restoration within four hours.
CONSTRUCTION CHECKS
Boreholes tested twice
Each borehole is pressure-tested twice before service.
TRANSPARENCY
Monthly portal data
Performance and outage data will be published monthly on the
resident portal.
11 / 12
Notes: This slide is about reducing uncertainty without pretending nothing can go wrong. The safeguards include physical separation, backup equipment, response targets, and monthly reporting.

## Slide 12
12 NEXT STEPS
What residents need to do next
SEP TO OCT 2026
Survey and enabling
works
Workdays 08:00 to 18:00.
NOV 2026 TO FEB 2027
Boreholes
Twelve sealed boreholes
installed and tested.
MAR TO MAY 2027
Building plant
Central heat pumps and
boosters installed.
JUN TO AUG 2027
Home connections
One working day per home.
15 SEP 2027
Full service starts
Network begins full service.
1
Confirm survey access
Allow the project team to check the
home connection requirements.
2
Choose a connection slot
Pick the one-day home connection
appointment when offered.
3
Clear radiator areas
Keep space around radiators clear
before the connection day.
12 / 12
Notes: The resident actions are simple: confirm access, choose the connection day, and keep radiator areas clear. The timeline also sets expectations for when work happens and when full service is planned to start.